ASSIGNMENT 4

AIM:
To design a CMOS inverter and
a. Calculate rise and fall time with and without load capacitor.
b. Plot VTC for DC input and calculate noise margin.
CIRCUIT:
CMOS inverter has been designed as follows -

OBSERVATIONS:
1. Vout and Vin wrt time

We find that with CL = 0.1u
Fall Time, Tf = 6.213165 x 10-2 s
Rise Time, Tr = 6.254552 x 10-2 s
Propagation Delay, TPHL = 7.151354 x 10-3 s
Propagation Delay, TPLH = 7.141256 x 10-3 s

We find that without CL
Fall Time, Tf = 6.199314 x 10-2 s
Rise Time, Tr = 6.195805 x 10-2 s
Propagation Delay, TPHL = 4.918616 x 10-7 s
Propagation Delay, TPLH = 4.719901 x 10-7 s

2. VTC

Since NGSPICE derivative function wasn’t working it was difficult to find out the noise margin.

CONCLUSION:
Addition of capacitive load increased the propagation delay by a large margin while the fall time was hardly affected.